## Slide 1: Risk Assessment
The basics

## Slide 2: Personal risk assessment
Ongoing before and throughout every activity we do !!!!
Do you do it ?
Crossing the road ? Mowing the lawn ?

## Slide 3: Level 1 Risk Assessment
A Level 1 Risk Assessment involves a review of the task by the PA in consultation with another Competent Person (normally the AA) to identify the hazards associated with the task and appropriate control measures required to manage these hazards

## Slide 4: Level 2 Risk Assessments
Must be carried out at any stage in the process where the PA, AA, a member of management or any other personnel believes that significant risks exist which will not be adequately controlled without a more rigorous assessment and the Application of additional controls.

## Slide 5: Why Level 2 ?
The task is new and unfamiliar
It is physically impossible to comply fully with the standards in a relevant local procedure, BP UK Upstream Region document or other recognised source of guidance
Previously used controls may not be reasonably practicable in this case
The task is complex and/or has potential impact on other activities

## Slide 6: Mandatory Level 2
Carrying out a Level 2 Risk Assessment is mandatory for the following activities:
Confined space entry including vessel/low Specific Activity (LSA) cleaning)
Naked flame hot work in all plant areas (hazardous or non-hazardous)
Failure to meet minimum isolations standard as defined in Safe Isolation and Reinstatement of Plant (SIRP) (in support of the isolation)
Deviation from an existing policy, procedure or practice

## Slide 7: What is risk ?
The combination of:
    Hazard
    Hazard effect (harm)
    Probability of the harm occurring

## Slide 8: How do we measure risk ?
Hazard Effect x Probability = Risk
He x P= R

## Slide 9: Identify the hazards.
Use checklists, experience and knowledge:
CHEMICALS
ASPHYXIANTS
DROWNING
BIOLOGICAL AGENTS
CONFINED SPACES
EXCAVATIONS
FALL OF PERSON FROM HEIGHT
FALL OF OBJECTS / MATERIAL FROM HEIGHT
TRIP OR FALL ON SAME LEVEL
MANUAL HANDLING
INCORRECT POSTURE
USE OF MACHINERY
MECHANICAL LIFTING
UNCONTROLLED RELEASE TO ENVIRONMENT
HAND TOOLS
STORED ENERGY
PRESSURE
IGNITION SOURCES (Inc. STATIC) / FIRE
EXPLOSION
ELECTRICITY
LIGHTING
CONTACT WITH HOT / COLD SURFACE
NOISE
VIBRATION
RADIATION
ADVERSE WEATHER

## Slide 10: Identify the effect.
1
2
3
4
5

## Slide 11: Identify the effect.
Be realistic, probabilities not possibilities.
Be holistic consider interactions of multiple risks.
Example : (Tolerance of risk)
Pakistan fatality (crane / vehicle movement
Example: (Risk perception regular activities)
Ula deck cargo movements, Transocean deck cargo (McLure similar incident within 3 months)

## Slide 12: Assess the probability.
Consider the following in order to decide upon
a realistic probability rating.
WHO?
WHY?
HOW LONG?
WHAT? WHEN?
HOW OFTEN?
WHERE?
HOW?
HOW MUCH?

## Slide 13: Probabilities

## Slide 14: Hazard & Probability Matrix

## Slide 15: Implementing Controls
Aim to reduce risk to:
As Low As Reasonably Practicable
(ALARP)
Hierarchy of controls (some are better than others)
Not all controls reduce Hazard Effect.
Some only reduce probability. (e.g. procedures, competency )
Some controls are Pre-requisite.
Other Controls are supplementary.

## Slide 16: Hierarchy of Controls

## Slide 17: Residual Risk
Re-visit the Hazard and re-assess against the Matrix
Allocate Risk Level
Is it ALARP
Residuals of:
>12 task should not proceed
9-12 Utmost caution
Consider interactions of multiple risks
Is further engineering input required?

## Slide 18: ALARP ?
Have all the controls been fully and effectively identified
Is there a need for engineering change to eliminate or reduce risk
Is there a need to shutdown the plant or process ?
Is the residual risk rating acceptable ?
Only then can you judge whether the risks are ALARP

## Slide 19: Controls
Implement pre-requisite controls
Ensure briefings cover all controls required
Complete task
Lessons Learned ?