## Slide 1: المحاضرة الخامسة الأدوات السبع المساعدة

## Slide 2: السبعة أدوات المساعدة
1- خرائط التدفق
2- خرائط المراقبة
3-خرائط باريتو
4- إستمارات التأكد
5- المدرج التكرارى
6- الرسم البيانى لعلاقة السبب بالنتيجة
7- الرسم المبعثر
Notes: We will explain now the seven tools that Ishikawa stated.
Theses too are the :
1. Histogram
2. Pareto Chart
3. Flowchart
4. Scatter Diagram
5. Cause and Effect Diagram
6. Check Sheets (data control)
7. Control Charts

## Slide 3: أدوات أخرى
خرائط الدورة
خرائط الترابط بين الأنشطة
Notes: We will explain some other tools also. These are:
Run Charts
Affinity Diagrams

## Slide 4: 1- المدرج التكرارى
0
20
40
60
80
100
0
5
10
15
20
25
30
35
40
45
50
55
60
وهو عبارة عن خريطة أعمدة تعرض توزيع البيانات
Notes: A Histogram is a vertical bar chart that depicts the distribution of a set of data. Unlike Run Charts or Control Charts, which are discussed in other modules, a Histogram does not reflect process performance over time. It's helpful to think of a Histogram as being like a snapshot, while a Run Chart or Control Chart is more like a movie.

## Slide 5: متى يتم إستخدام المدرج التكرارى؟
يلخص مجموعات كبيرة من البيانات بطريقة الرسوم البيانية0
يقارن ما بين نتائج العملية وحدود المواصفات0
ينقل المعلومات للفريق0
يساعد فى عملية إتخاذ القرار0
Notes: When you are unsure what to do with a large set of measurements presented in a table, you can use a Histogram to organize and display the data in a more user friendly format. A Histogram will make it easy to see where the majority of values fails in a measurement scale, and how much variation there is. It is helpful to construct a Histogram when you want to do the following:
Summarize large data sets graphically. When you look at a histogram, you can see that a set of data presented in a table isn't easy to use. You can make it much easier to understand by summarizing it on a tally sheet and organizing it into a Histogram
Compare process results with specification limits. If you add the process specification limits to your Histogram, you can determine quickly whether the current process was able to produce "good" products. Specification limits may take the form of length, weight, density, quantity of materials to be delivered, or whatever is important for the product of a given process. A Histogram shows on which the specification limits, or "goalposts," have been superimposed. We'll look more closely at the implications of specification limits when we discuss Histogram interpretation later in this module.
Communicate information graphically. The team members can easily see the values which occur most frequently. When you use a Histogram to summarize large data sets, or to compare measurements to specification limits, you are employing a powerful tool for communicating information.
Use a tool to assist in decision making. As you will see as we move along through this module, certain shapes, sizes, and the spread of data have meanings that can help you in investigating problems and making decisions. But always bear in mind that if the data you have in hand aren't recent, or you don't know how the data were collected, it's a waste of time trying to chart them. Measurements cannot be used for making decisions or predictions when they were produced by a process that is different from the current one, or were collected under unknown conditions.

## Slide 6: الأجزاء المكونة للمدرج التكرارى
5
4
2
3
1
0
20
40
60
80
100
0
5
10
15
20
25
30
35
40
45
50
55
60
التكرارية
أيام التشغيل
أيام التشغيل السابقة لفشل مستقبل HF
1
3
2
4
Mean time between failure (in days) for r-1051 HF receiver
Data taken at SIMA, pearl harbor, 15 May- 15 July 94
5
العنوان
الأعمدة
المحور الأفقى X
المحور الرأسى Y
معلومات إضافية
Notes: As you can see in the figure above, a Histogram is made up of five parts:
1. Title: The title briefly describes the information that is contained in the Histogram.
2. Horizontal or X-Axis: The horizontal or X-axis shows you the scale of values into which the measurements fit. These measurements are generally grouped into intervals to help you summarize large data sets. Individual data points are not displayed.
3. Bars: The bars have two important characteristics-height and width. The height represents the number of times the values within an interval occurred. The width represents the length of the interval covered by the bar. It is the same for all bars.
4. Vertical or Y-Axis.. The vertical or Y-axis is the scale that shows you the number of times the values within an interval occurred. The number of times is also referred to as “ frequency.”
5. Legend: The legend provides additional information that documents where the data came from and how the measurements were gathered.

## Slide 7: بناء المدرج التكرارى
الخطوة الأولى : عد عدد نقاط البيانات0
الخطوة الثانية : لخص البيانات فى ورقة العد0
الخطوة الثالثة : إحسب المدى لمجموعة البيانات0
الخطوة الرابعة : حدد عدد الفترات المطلوبة0
الخطوة الخامسة : إحسب عرض الفترات0
Notes: There are many different ways to organize data and build Histograms. You can safely use any of them as long as you follow the basic rules. In this module, we use the nine-step approach which will be describe

## Slide 8: بناء المدرج التكرارى
الخطوة السادسة : حدد نقاط البداية لكل فترة0
الخطوة السابعة : عد عدد النقاط فى كل فترة0
الخطوة الثامنة : عين موقع البيانات0
الخطوة التاسعة : أضف العنوان والمعلومات الإضافية0

## Slide 9: كيفية بناء المدرج التكرارى
الخطوة الأولى : عد عدد نقاط البيانات
Number of yards long (+ data) and yards short (-data) that a gun crew missed its target.
Total = 135
-180
-10
-130
260
160
210
50
140
210
-30
300
110
260
110
30
30
220
190
180
40
20
220
130
80
260
-30
70
130
190
60
170
-100
240
70
30
-40
350
270
20
50
100
120
380
230
130
150
260
-70
280
290
250
320
40
240
140
30
330
90
-50
210
-20
250
410
90
-20
30
-20
180
80
70
140
120
-80
140
-80
360
70
100
230
240
250
50
190
160
10
180
-130
30
120
-10
-30
180
120
310
130
100
270
50
100
130
80
-60
20
340
130
100
40
200
270
10
250
110
150
240
-30
130
20
-30
20
200
280
140
-90
180
200
370
130
200
170
80
210
70
190
60
80
Notes: Step 1 - Count the total number of data points you have listed. Suppose your team collected data on the miss distance for the gunnery contest. The data you collected was for the fall of shot both long and short of the target. The data are displayed in the figure above Simply counting the total number of entries in the data set completes this step. In this example, there are 135 data points.

## Slide 10: كيفية بناء المدرج التكرارى
الخطوة الثانية : لخص البيانات فى ورقة العد
Data Tally Data Tally Data Tally Data Tally Data Tally
-180
-130
-100
-90
-80
-70
-60
-50
-40
-30
1
2
1
1
2
1
1
1
1
5
-20
-10
10
20
30
40
50
60
70
80
3
2
2
5
6
3
4
2
5
5
90
100
110
120
130
140
150
160
170
180
2
5
3
4
8
5
2
2
2
5
190
200
210
220
230
240
250
260
270
280
4
4
4
2
2
4
4
4
3
2
290
300
310
320
330
340
350
360
370
380
410
1
1
1
1
1
1
1
1
1
1
1
Notes: Step 2 - Summarize your data on a tally sheet. You need to summarize your data to make it easy to interpret. You can do this by constructing a tally sheet.
First, identify all the different values found in this figure (-160, -010. . .030, 220, etc.).
Organize these values from smallest to largest (-1 80, -120.. .380, 410).
Then, make a tally mark next to the value every time that value is present in the data set.
Alternatively, simply count the number of times each value is present in the data set and enter that number next to the value.
This tally helped us organize 135 mixed numbers into a ranked sequence of 51 values. Moreover, we can see very easily the number of times that each value appeared in the data set. This data can be summarized even further by forming intervals of values.

## Slide 11: كيفية بناء المدرج التكرارى
الخطوة الثالثة : إحسب المدى لمجموعة البيانات
أكبر قيمة = 410 ياردة بعد الهدف
أصغر قيمة = 180 ياردة أقل من الهدف
مدى القيم = 590 ياردة
الحساب : = + 410 – (- 180) = 410 + 180 = 590
Notes: Step 3 - Compute the range for the data set. Compute the range by subtracting the smallest value in the data set from the largest value. The range represents the extent of the measurement scale covered by the data; it is always a positive number. The range for the data in the figure is 590 yards. This number is obtained by subtracting -1 80 from +410. The mathematical operation broken down is:
+410 - (-180) = 410 + 180 = 590
Remember that when you subtract a negative (-) number from another number it becomes a positive number.

## Slide 12: كيفية بناء المدرج التكرارى
الخطوة الرابعة : حدد عدد الفترات المطلوبة
إستخدم هذا العدد من الفترات
إذا كان لديك هذا العدد الكبير
من نقاط البيانات
أقل من 50 فترات من 5 إلى 7
من 50 إلى 99 فترات من 6 إلى 10
من 250 إلى 100 فترات من 7 إلى 12
أكثر من 250 فترات من 10 إلى 20
Notes: Step 4 - Determine the number of intervals required. The number of intervals influences the pattern, shape, or spread of your Histogram. Use the following table to determine how many intervals (or bars on the bar graph) you should use.
If you have this Use this number
many data points. of intervals:
Less than 50 5 to 7
50 to 99 6 to 10
1 00 to 250 7 to 12
More than 250 10 to 20
For this example, 10 has been chosen as an appropriate number of intervals.

## Slide 13: كيفية بناء المدرج التكرارى
الخطوة الخامسة : إحسب عرض الفترات
عرض الفترة
=
=
590
10
=
المدى
عدد الفترات
59
قرب العدد
إلى 60
إستخدم الرقم 10
لعدد الفترات
Notes: Step 5 - Compute the interval width. To compute the interval width divide the range (590) by the number of intervals (10). When computing the interval width, you should round the data up to the next higher whole number to come up with values that are convenient to use. For example, if the range of data is 17, and you have decided to use 9 intervals, then your interval width is 1.88. You can round this up to 2.
In this example, you divide 590 yards by 10 intervals, which gives an interval width of 59. This means that the length of every interval is going to be 59 yards. To facilitate later calculations, it is best to round off the value representing the width of the intervals. In this case, we will use 60, rather than 59, as the interval width.

## Slide 14: كيفية بناء المدرج التكرارى
الخطوة السادسة : حدد نقاط البداية لكل فترة
الخطوة السابعة : عد عدد النقاط فى كل فترة
عدد العد قيمة النهاية عرض الفترة قيمة البداية عدد الفترات
1
2
3
4
5
6
7
8
9
10
-180
-120
-60
000
060
120
180
240
300
360
60
60
60
60
60
60
60
60
60
60
-120
-060
000
060
120
180
240
300
360
420
3
5
13
20
22
24
20
18
6
4
مساوى أو أكبر من
قيمة البداية
ولكن أقل من
قيمة النهاية
Notes: Step 6 - Determine the starting point for each interval. Use the smallest data point in your measurements as the starting point of the first interval. The starting point for the second interval is the sum of the smallest data point and the interval width. For example, if the smallest data point is -180, and the interval width is 60, the starting point for the second interval is -120. Follow this procedure to determine all of the starting points (-180 + 60 = -120; -120 + 60 = -60; etc.).
Step 7 - Count the number of points that fall within each interval. These are the data points that are equal to or greater than the starting value and less than the ending value. For example, if the first interval begins with -1 80 and ends with -1 20, all data points that are equal to or greater than -1 80, but still less than -1 20, will be counted in the first interval. Keep in mind that EACH DATA POINT can appear in only one interval.

## Slide 15: كيفية بناء المدرج التكرارى
الخطوة الثامنة : عين موقع البيانات
الخطوة التاسعة : أضف العنوان والمعلومات الإضافية
0
5
10
15
20
25
-180
-120
-60
000
060
120
180
240
300
360
420
S
H
O
T
C
O
U
N
T
YARDS SHORT
YARDS LONG
TARGET
MISSES
HITS
MISSES
MISS DISTANCE FOR MK 75 GUN TEST FIRING
Notes: Step 8 - Plot the data. A more precise and refined picture comes into view once you plot your data. You bring all of the previous steps together when you construct the graph.
The horizontal scale across the bottom of the graph contains the intervals that were calculated previously.
The vertical scale contains the count or frequency of observations within each of the intervals.
A bar is drawn for the height of each interval. The bar's look like columns.
The height is determined by the number of observations or percentage of the total observations for each of the intervals.
The Histogram may not be perfectly symmetrical. Variations will occur. Ask yourself whether the picture is reasonable and logical, but be careful not to let your preconceived ideas influence your decisions unfairly.
Step 9 - Add the title and legend. A title and a legend provide the who, what, when, where, and why that are important for understanding and interpreting the data. This additional information documents the nature of the data, where it came from, and when it was collected. The legend may include such things as the sample size, the dates and times involved, who collected the data, and identifiable equipment or work groups. It is important to include any information that helps clarify what the data describes.

## Slide 16: تفسير المدرجات التكرارية
المواقع وإنتشار البيانات
الهدف
A
الهدف
B
الهدف
C
الهدف
D
Notes: A Histogram provides a visual representation so you can see where most of the measurements are located and how spread out they are. Your Histogram might show any of the following conditions:
Most of the data were on target, with very little variation from it, as in the figure (A).
Although some data were on target, many others were dispersed away from the target, as in figure (B)
Even when most of the data were close together, they were located off the target by a significant amount, as in the figure (C).
The data were off target and widely dispersed, as in the figure (D).
This information helps you see how well the process performed and how consistent it was. You may be thinking, "So what? How will this help me do my job better'.?" Well, with the results of the process clearly depicted, we can find the answer to a vital question:

## Slide 17: تفسير المدرجات التكرارية
الهدف
هل العملية فى نظام حدود المواصفات(LSL)؟
الهدف
داخل نطاق الحدود
OUT OF SPEC
USL
LSL
USL
LSL
حد المواصفات السفلى LSL=
حد المواصفات العلوى USL=
Notes: Looking at the Histogram, you can see, not only whether you were within specification limits, but also how close to the target you were.

## Slide 18: تفسير المدرجات التكرارية
تغير العملية
اليوم الأول
الهدف
الهدف
اليوم الثانى
الهدف
اليوم الثالث
الهدف
اليوم الرابع
Notes: Portraying your data in a Histogram enables you to check rapidly on the number, or the percentage, of defects produced during the time you collected data. But unless you know whether the process was stable, you won't be able to predict whether future products will be within specification limits or determine a course of action to ensure that they are.
A Histogram can show you whether or not your process is producing products or services that are within specification limits. To discover whether the process is stable, and to predict whether it can continue to produce within spec limits, you need to use a Control Chart (see the Control Chart module). Only after you have discovered whether your process is in or out of control can you determine an appropriate course of action-to eliminate special causes of variation, or to make fundamental changes to your process.

## Slide 19: تفسير المدرجات التكرارية
الأشكال الشائعة للمدرج التكرارى
منحرف
(غير متناسق)
غير مكتمل
متناسق
Notes: There are times when a Histogram may look unusual to you. It might have more than one peak, be discontinued, or be skewed, with one tail longer than the other, as shown in the figure. In these circumstances, the people involved in the process should ask themselves whether it really is unusual. The Histogram may not be symmetrical, but you may find out that it should look the way it does. On the other hand, the shape may show you that something is wrong, that data from several sources were mixed, for example, or different measurement devices were used, or operational definitions weren't applied. What is really important here is to avoid jumping to conclusions without properly examining the alternatives.

## Slide 20: ورقة عمل
الخطوة الأولى : عد عدد نقاط البيانات
الرقم الإجمالى =
Notes: The worksheet should like this.

## Slide 21: ورقة عمل
لخص البيانات فى ورقة العد
Value
Value
Value
Value
Value
Tally
Tally
Tally
Tally
Tally
Notes: Detail it as shown

## Slide 22: ورقة عمل
الخطوة الثالثة : إحسب المدى لمجموعة البيانات
أكبر قيمة = -----------------
أصغر قيمة = -----------------
مدى القيمة = -----------------
Notes: Write the largest, smallest and range of value of the data set

## Slide 23: ورقة عمل
الخطوة الرابعة : حدد عدد الفترات المطلوبة
إستخدم هذا العدد من الفترات
إذا كان لديك هذا العدد الكبير
من نقاط البيانات
أقل من 50 فترات من 5 إلى 7
من 50 إلى 99 فترات من 6 إلى 10
من 250 إلى 100 فترات من 7 إلى 12
أكثر من 250 فترات من 10 إلى 20
Notes: Use the number of intervals according to the data points as described above

## Slide 24: ورقة عمل
الخطوة الخامسة : إحسب عرض الفترات
عرض الفترات
=
=
=
المدى
عدد الفترات
قرب العدد لأعلى
رقم تالى كامل
Notes: Compute the interval points as shown

## Slide 25: ورقة عمل
الخطوة السادسة : حدد نقاط البداية لكل فترة
الخطوة السابعة : عد عدد النقاط فى كل فترة
عدد الفترات
قيمة البداية
عرض الفترة
قيمة النهاية
عدد العد
1
2
3
4
5
6
7
8
9
10
Notes: Determine the starting point of each interval and count the number of points in each interval

## Slide 26: ورقة عمل
الخطوة الثامنة : عين موقع البيانات
الخطوة التاسعة : أضف العنوان والمعلومات الإضافية
Notes: Plot the data and add the title and legend

## Slide 27: ورشة عمل

## Slide 28: التمرين الأول : مفتاح الحل
الخطوة الأولى : عد عدد نقاط البيانات
11
4
8
23
24
11
14
17
22
14
11
12
10
20
20
11
15
11
23
10
16
15
11
15
7
16
14
16
18
13
19
11
13
18
16
17
22
9
10
15
20
32
10
24
15
18
17
16
25
5
10
11
13
22
15
12
12
16
21
20
19
16
12
28
16
17
26
9
15
18
17
14
19
10
10
13
24
9
11
13
Total = 80
Notes: Here’s an exercise that describes these steps accurately

## Slide 29: التمرين الأول : مفتاح الحل
الخطوة الثانية : لخص البيانات فى ورقة العد
% fat
0
1
2
3
4
5
6
7
8
9
10
No. of pers.
0
0
0
0
1
1
0
1
1
3
7
% fat
11
12
13
14
15
16
17
18
19
20
21
No. of pers.
9
4
5
4
7
8
5
4
3
4
1
% fat
22
23
24
25
26
27
28
29
30
31
32
No. of pers.
3
2
3
1
1
0
1
0
0
0
1

## Slide 30: التمرين الأول : مفتاح الحل
الخطوة الثالثة : إحسب المدى لمجموعة البيانات
أكبر قيمة = 23 % دهون الجسم
أصغر قيمة = 4 % دهن الجسم
مدى القيم = 28% دهون بالجسم

## Slide 31: التمرين الأول : مفتاح الحل
الخطوة الرابعة : حدد عدد الفترات المطلوبة
إستخدم هذا العدد من الفترات
إذا كان لديك هذا العدد الكبير
من نقاط البيانات
أقل من 50 فترات من 5 إلى 7
من 50 إلى 99 فترات من 6 إلى 10
من 250 إلى 100 فترات من 7 إلى 12
أكثر من 250 فترات من 10 إلى 20

## Slide 32: التمرين الأول : مفتاح الحل
الخطوة الخامسة : إحسب عرض الفترات
عرض الفترة
=
=
28
8
=
المدى
عدد الفترات
5ر3
قرب العدد
إلى 4
إستخدم الرقم 10
لعدد الفترات

## Slide 33: التمرين الأول : مفتاح الحل
الخطوة السادسة : حدد نقاط البداية لكل فترة
الخطوة السابعة : عد عدد النقاط فى كل فترة
عدد الفترات
قيمة البداية
عرض الفترة
قيمة النهاية
عدد العد
1
4
+4
8
3
2
8
+4
12
20
3
12
+4
16
20
4
16
+4
20
20
5
20
+4
24
10
6
24
+4
28
5
7
28
+4
32
1
8
32
+4
36
1
مساوى أو أكبر من
قيمة البداية
ولكن أقل من
قيمة النهاية

## Slide 34: التمرين الأول : مفتاح الحل
الخطوة الثامنة : عين موقع البيانات
الخطوة التاسعة : أضف العنوان والمعلومات الإضافية
20
18
16
14
12
10
8
6
4
2
0
0 4 8 12 16 20 24 28 32 36
PERCENT BODY FAT
Satisfactory % BODY FAT
June 94 PRT percent body fat
NO. OF PERSONNEL

## Slide 35: التمرين الثانى
Notes: A Marine Corps small arms instructor was performing an analysis of 9 mm pistol marksmanship scores to improve training methods. For every class of 25, the instructor recorded the scores for each student who occupied the first four firing positions at the small arms range. The instructor then averaged the scores for each class, maintaining a database on 105 classes. These are the data collected

## Slide 36: التمرين الثانى : مفتاح الحل
الخطوة الأولى : عد عدد نقاط البيانات
Total = 105
160
175
270
180
255
255
230
195
220
210
220
190
190
265
245
180
245
255
235
215
240
230
155
210
255
270
260
210
235
230
225
215
225
300
225
235
200
240
225
195
215
250
230
215
280
275
170
200
245
225
220
225
220
220
225
185
240
175
220
170
235
210
235
245
225
250
170
185
265
205
230
235
225
195
200
285
185
195
270
260
230
240
200
235
235
200
215
200
250
215
195
200
245
225
215
165
220
260
230
185
225
220
230
230
240

## Slide 37: التمرين الثانى : مفتاح الحل
الخطوة الثانية : لخص البيانات فى ورقة العد
score
155
160
165
170
175
180
185
190
195
200
tally
1
1
1
3
2
2
4
2
5
7
score
205
210
215
220
225
230
235
240
245
250
tally
1
4
7
8
11
9
8
5
5
3
score
255
260
265
270
275
280
285
290
295
300
tally
4
3
2
3
1
1
1
0
0
1

## Slide 38: التمرين الثانى : مفتاح الحل
الخطوة الثالثة : إحسب المدى لمجموعة البيانات
أكبر قيمة = 300 نقطة
أصغر قيمة = 155 نقطة
مدى القيم = 145 نقطة

## Slide 39: التمرين الثانى : مفتاح الحل
الخطوة الرابعة : حدد عدد الفترات المطلوبة
إستخدم هذا العدد من الفترات
إذا كان لديك هذا العدد الكبير
من نقاط البيانات
أقل من 50 فترات من 5 إلى 7
من 50 إلى 99 فترات من 6 إلى 10
من 250 إلى 100 فترات من 7 إلى 12
أكثر من 250 فترات من 10 إلى 20

## Slide 40: التمرين الثانى : مفتاح الحل
الخطوة الخامسة : إحسب عرض الفترات
عرض الفترات
=
=
145
10
=
المدى
عدد الفترات
5ر14
قرب العدد
إلى15
إستخدم الرقم 10
لعدد الفترات

## Slide 41: التمرين الثانى : مفتاح الحل
الخطوة السادسة : حدد نقاط البداية لكل فترة
الخطوة السابعة : عد عدد النقاط فى كل فترة
عدد الفترات
قيمة البداية
عرض الفترة
قيمة النهاية
عدد العد
1
155
+15
170
3
2
170
+15
185
7
3
185
+15
200
11
4
200
+15
215
12
5
215
+15
230
26
6
230
+15
245
22
7
245
+15
260
12
8
260
+15
275
8
مساوى أو أكبر من
قيمة البداية
ولكن أقل من
قيمة النهاية
275
9
+15
290
3
10
290
+15
300
1

## Slide 42: التمرين الثانى : مفتاح الحل
الخطوة الثامنة : عين موقع البيانات
الخطوة التاسعة : أضف العنوان والمعلومات الإضافية
Marksmanship scores for 9mm PISTOL
0
5
10
15
20
25
155
170
185
200
215
245
230
260
275
290
300
30
SCORES
NO. OF PERSONNEL